## Slide 1: Name: Amr Hossam Mohamed Younes
Internship
Final Project

## Slide 2: AGENDA
Project Overview
System Architecture
Testbenches
Bitstream Generation for FPGA

## Slide 3: Project Overview

## Slide 4: Matrix 3x3 inversion using QR decomposition
QR decomposition
Simple matrix inversion
multiplication
Simple matrix transpose

## Slide 5: Matric 3x3 inversion using QR decomposition
Pivot Selection:
  Start with the element a as the pivot. We want to nullify the element d below it.
CORDIC Vectoring for a and d:
  Use a and d as inputs to the vectoring CORDIC algorithm.
  This will result in a new value a′ and an angle θ1​.
CORDIC Rotation for Other Elements:
  Step 1: Apply θ1​ to b and e using rotational CORDIC, resulting in b′ and e′.
  Step 2: Apply θ1​ to c and f using rotational CORDIC, resulting in c′ and f′.

## Slide 6: Matric 3x3 inversion using QR decomposition
4.Update Matrix:
The element d is now nulled in the R-matrix, and the other elements a′, b′, c′, e′, f′ are updated accordingly.
5.Repeat Process for Lower Rows:
Perform the same operation on the elements g and h and updating their corresponding rows using rotational CORDIC.
6.Resulting Matrix:
After completing these operations, the matrix transforms into the upper triangular R matrix.
The angles θ obtained at each step are used to construct the orthogonal matrix Q.

## Slide 7: Matric 3x3 inversion using QR decomposition
7.Optainig Q by multiply Q1, Q2, Q3 To get Q
8.Get R inverse and Q transpose multiply them together and you will get A inverse

## Slide 8: System Architecture

## Slide 9: System Architecture
Cordic Vectoring
The CORDIC vectoring algorithm takes two inputs, x and y, and performs the following:
  It aims to rotate the vector (x, y) such that the output y′ becomes zero.
  The output consists of the new x value, after the necessary rotations, along with the angle θ used for the rotation.

## Slide 10: System Architecture
Cordic Vectoring

## Slide 11: System Architecture
Cordic Rotational
  It aims to rotate the vector (x, y) with angle θ.
  The output consists of the new x value and new y value after the necessary rotations, along with the angle θ used for the rotation.

## Slide 12: System Architecture
Cordic Rotational

## Slide 13: System Architecture

## Slide 14: System Architecture
FSM

## Slide 15: Testbenches

## Slide 16: Testbenches
CORDIC Rotational Module
  testbench verifies the functionality of the CORDIC rotational module by calculating the expected outputs (rotated coordinates) using a Python and give it to the testbench.

## Slide 17: Testbenches
CORDIC Vectoring Module
  testbench verifies the functionality of the CORDIC Vectoring module by calculating the expected magnitude and angle using a Python and give it to the testbench.

## Slide 18: Testbenches
Top Module
  Inputs are provided, and the expected outputs are calculated using an online tool, such as the matrix calculator, for validation.

## Slide 19: Bitstream Generation for FPGA

## Slide 20: Bitstream Generation for FPGA
  Target Frequency: 150 MHz
  Target Board: Zynq UltraScale+ MPSoC ZCU104 Evaluation Kit
  Successfully generated the bitstream for the ZCU104 board to meet the 150 MHz design target.
  Total chip power: 0.592 W

## Slide 21: THANK YOU